Jun 18th, 2014:
This file is deprecated: everything has been inserted in the “XtremWeb-HEP Introduction” document
XtremWeb-HEP 8 – Offering and Billing
Specifications
Types of Metrics
–	The 'apps' and 'works' tables should both contain Offering Metrics, whose value is known before any task run,
–	The 'works' table should also contain Billing Metrics, whose value is known after the end of the work.
Offering Metrics
These metrics specify resource characteristics required by the application (independently of any specific work), or by the work (with higher values).
For example, an application may require 512 MB RAM, and a specific work processing much data may require 3.000 MB RAM.
– minMemory :	Minimum amount of RAM per core (in MB),
– minCPUSpeed :	Minimum CPU speed (in MHz),
– minFreeMassStorage :	Minimum free mass storage (in GB),
– maxWallClockTime :	Maximum wall clock time (in seconds) only for works,
apps.minFreeMassStorage is calculated using the sum of 'datas.size' of following pointers :
– defaultStdinURI :	STDIN if not provided by the work,
– baseDirinURI :	Input files which are always sent with the work,
– defaultDirinURI :	Additional input files if not provided by the work,
– max of 'datas.size' of all binary URIs,
– max of 'datas.size' of all library URIs.
works.minFreeMassStorage has a minimum value calculated using 'datas.size' of pointers from the 'apps' table and 'datas.size' of following pointers:
– stdinURI :	overrides 'apps.defaultStdinURI',
– dirinURI :	overrides 'apps.defaultDirinURI'.
This metric may be provided by the submitter of the work in order to reserve storage space also for output files.
Billing Metrics
These metrics provide real resource consumption the work :
– status :	Depending on work status and SLA,
the work will be billed or not,
– resultURI :	Its 'datas.size' is the global size of all output files,
– (compenddate – compstartdate) :	Wall clock duration of the work.